## Slide 2
Scope and Motivation
Recovery Strategies
Performance Model
Cost Model
Tradeoffs & Comparisons

## Slide 3: Motivation for 1st stage reuse: Cost savings with reasonable technical challenge
Launch vehicle reuse is often touted as a key step to reduce costs and increase launch rate.
However, whole-vehicle reuse architectures face major technical challenges, and none have survived development.
  e.g. early STS architectures, X-33, Delta Clipper
Reusing only the 1st stage (or part of the 1st stage) is an easier, incremental step
Expendable launch vehicles
Partially reusable launch vehicles
Fully reusable launch vehicles
High development cost
Potential cost savings
Demonstrated technology
Incremental development from existing vehicles
High cost/flight
now
future?

## Slide 4: Why focus on 1st stage reusability? Best reward/effort ratio
The first stage is easier to recover …
… and embodies the majority of the production cost
1st stage reuse is therefore of considerable commercial interest
1st stage
2nd stage
Reentry specific energy
~2 MJ kg-1
~60 MJ kg-1
1st stage
2nd stage
Production cost
TODO
SpaceX
Falcon 9
Operational
Blue Origin
New Glenn
In development
ULA
Vulcan SMART reuse
In development
Boeing
XS-1 Phantom Express
In development

## Slide 5: Wide variety of 1st stage reuse proposals & implementations
Parachute recovery
(e.g. Shuttle*, Ares I)
Image: NASA
Image: ULA
Engine-pod recovery
(e.g. Vulcan SMART, Ariane Adeline)
Image: Khrunichev
Air-breathing flyback
(e.g. Baikal, LFBB)
Propulsive landing
(e.g. Falcon 9*, New Glenn)
*reused successfully
Image: SpaceX

## Slide 6: There is considerable debate in industry over the value of 1st stage reuse
“… SpaceX will therefore not break even on the reusability portion of the equation.”
- Jim Cantrell, CEO Vector Space Systems, 2017
“We tried to make [the SSME] reusable […] Look how long and how much money it took for us to do that”
- Dan Dumbacher, NASA, 2014
“I am a skeptic with regard to many of the claims that have been made for cost reductions.”
- David Thompson, CEO Orbital ATK, 2016
“ [the launch industry] is going to be dominated by reusability”
- Bob Smith, CEO Blue Origin, 2018
“the potential cost reduction over the long term is probably in excess of a factor of 100.”
- Elon Musk, CEO SpaceX, 2015

## Slide 7: Fundamental questions
Tradeoff between payload capacity and production cost savings:
  Recovery requires extra hardware (& maybe propellant) on the first stage
   A reusable vehicle will have lower payload capacity than an “equivalent” expendable vehicle
Uncertain refurbishment costs
Uncertain market demand
Which reuse architecture, if any, can provide sufficient cost savings to justify its associated payload reduction?
How do expected cost savings vary with refurbishment costs and launch rate?

## Slide 8: Scope
We consider orbital launch vehicles using
2 sequential stages
Proven, high-TRL propulsion and structural technologies
For such launch vehicles, we
Identify and categorize strategies for recovering & reusing (portions of) the first stage
Estimate the effect of each strategy on payload capacity
Estimate the effect of each strategy on operations, production and development costs
Identify tradeoffs and compare strategies

## Slide 9: Approach
Use statistical techniques to represent the uncertainty inherent in high-level performance and cost models
  Performance/payload model: derived from physical first principles
  Cost model: TRANSCOST 8.2
Wherever possible, these models are calibrated against data from
  Operational launch vehicles
  Detailed conceptual studies
Compare reusable boosters against the baseline of an “equivalent” expendable vehicle

## Slide 10: Classifying recovery strategies
Choice | Option 1 | Option 2 | Option 3 | Option 4 | Option 5
Portion of booster recovered | Fraction of booster mass recovered: Full: Partial, engines: |  |  |  | 
Recovery location | Launch site | Downrange - ocean | Downrange - ship | Downrange - land | Downrange - mid-air
Recovery propulsion method | Rocket | Air-breathing | None |  | 
Landing method | Propulsive (vertical) | Winged (horizontal) | Parachute |  | 
Choice | Option 1 | Option 2 | Option 3 | Option 4 | Option 5
Portion of booster recovered |  |  |  |  | 
Recovery location | Launch site | Downrange - ocean | Downrange - ship | Downrange - land | Downrange - mid-air
Recovery propulsion method | Rocket | Air-breathing | None |  | 
Landing method | Propulsive (vertical) | Winged (horizontal) | Parachute |  | 
90 possible choice combinations, of which 36 pass “laugh test”
Classification captures all 10 operated or proposed recovery strategies known to the authors

## Slide 11: Identifying recovery strategies
Rocket
Air-breathing
None
Launch site
Propulsive (vertical)
Winged (horizontal)
Insufficient energy for return if staging velocity > ~1 km/s
Parachute
Recovery Propulsion Method
Recovery Location
Landing Method
Downrange - ocean
Downrange - ship
e.g. Falcon 9
e.g. USAF RBS
High landing loads
Propulsive (vertical)
Winged (horizontal)
Parachute
Winged landing preferable
e.g. Baikal, LFBB
High landing loads
Rocket
Air-breathing
None
Propulsion not needed
Propulsive (vertical)
Winged (horizontal)
Parachute
e.g. Shuttle, Ares I
Rocket
Air-breathing
None
Propulsive (vertical)
Winged (horizontal)
Parachute
e.g. Falcon 9
Targeting difficult
Propulsion not needed for winged vehicles
Propulsive (vertical)
Winged (horizontal)
Parachute
e.g. New Glenn
Only small boosters
Full Recovery Partial Recovery
e.g. Adeline
Plausible
Plausible
Plausible
Propul. not needed for winged vehicles
Plausible
Plausible
Plausible
Plausible
Targeting difficult
Only small boosters
Targeting difficult
Plausible
Portion of Booster Recovered
Operated
Plausible
Major challenges
Not desirable
Color code:

## Slide 12: Identifying recovery strategies (2)
Downrange - land
Downrange – mid-air
Rocket
Air-breathing
None
Propulsion not needed
Propulsive (vertical)
Winged (horizontal)
Parachute
Plausible
None
Propulsive (vertical)
Winged (horizontal)
Parachute
e.g. Sippel et al 2017
Plausible
High landing loads
Rocket
Air-breathing
Propulsion not needed
Capture difficult
e.g. ULA SMART
Only small boosters
Recovery Propulsion Method
Recovery Location
Landing Method
Full Recovery Partial Recovery
Portion of Booster Recovered
Plausible
e.g. XS-1 Phantom Express
Operated
Plausible
Major challenges
Not desirable
Color code:

## Slide 13: Identifying recovery strategies (3)
Launch site recovery
Downrange recovery
Falcon 9
USAF RBS
Baikal
Falcon 9
New Glenn
Ares I
XS-1 Phantom Express
Vulcan SMART
Examples: