## Slide 2
Scope and Motivation
Recovery Strategies
Performance Model
Cost Model
Tradeoffs & Comparisons

## Slide 3
Scope and Motivation
Recovery Strategies
Performance Model
Cost Model
Tradeoffs & Comparisons

## Slide 4: Motivation for 1st stage reuse: Cost savings with reasonable technical challenge
Launch vehicle reuse is often touted as a key step to reduce costs and increase launch rate.
However, whole-vehicle reuse architectures face major technical challenges, and none have survived development.
  e.g. early STS architectures, X-33, Delta Clipper
Reusing only the 1st stage (or part of the 1st stage) is an easier, incremental step
Expendable launch vehicles
Partially reusable launch vehicles
Fully reusable launch vehicles
High development cost
Potential cost savings
Demonstrated technology
Incremental development from existing vehicles
High cost/flight
now
future?

## Slide 5: Why focus on 1st stage reusability? Best reward/effort ratio
The first stage is easier to recover …
… and embodies the majority of the production cost
1st stage reuse is therefore of considerable commercial interest
1st stage
2nd stage
Reentry specific energy
~2 MJ kg-1
~60 MJ kg-1
1st stage
2nd stage
Production cost
TODO
SpaceX
Falcon 9
Operational
Blue Origin
New Glenn
In development
ULA
Vulcan SMART reuse
In development
Boeing
XS-1 Phantom Express
In development

## Slide 6: Wide variety of 1st stage reuse proposals & implementations
Parachute recovery
(e.g. Shuttle*, Ares I)
Image: NASA
Image: ULA
Engine-pod recovery
(e.g. Vulcan SMART, Ariane Adeline)
Image: Khrunichev
Air-breathing flyback
(e.g. Baikal, LFBB)
Propulsive landing
(e.g. Falcon 9*, New Glenn)
*reused successfully
Image: SpaceX

## Slide 7: There is considerable debate in industry over the value of 1st stage reuse
“… SpaceX will therefore not break even on the reusability portion of the equation.”
- Jim Cantrell, CEO Vector Space Systems, 2017
“We tried to make [the SSME] reusable […] Look how long and how much money it took for us to do that”
- Dan Dumbacher, NASA, 2014
“I am a skeptic with regard to many of the claims that have been made for cost reductions.”
- David Thompson, CEO Orbital ATK, 2016
“ [the launch industry] is going to be dominated by reusability”
- Bob Smith, CEO Blue Origin, 2018
“the potential cost reduction over the long term is probably in excess of a factor of 100.”
- Elon Musk, CEO SpaceX, 2015

## Slide 8: Fundamental questions
Tradeoff between payload capacity and production cost savings:
  Recovery requires extra hardware (& maybe propellant) on the first stage
   A reusable vehicle will have lower payload capacity than an “equivalent” expendable vehicle
Uncertain refurbishment costs
Uncertain market demand
Which reuse architecture, if any, can provide sufficient cost savings to justify its associated payload reduction?
How do expected cost savings vary with refurbishment costs and launch rate?

## Slide 9: Scope
We consider orbital launch vehicles using
2 sequential stages
Proven, high-TRL propulsion and structural technologies
For such launch vehicles, we
Identify and categorize strategies for recovering & reusing (portions of) the first stage
Estimate the effect of each strategy on payload capacity
Estimate the effect of each strategy on operations, production and development costs
Identify tradeoffs and compare strategies

## Slide 10: Approach
Use statistical techniques to represent the uncertainty inherent in high-level performance and cost models
  Performance/payload model: derived from physical first principles
  Cost model: TRANSCOST 8.2
Wherever possible, these models are calibrated against data from
  Operational launch vehicles
  Detailed conceptual studies
Replicability
  Open code TODO github link
  Open data
Compare reusable boosters against the baseline of an “equivalent” expendable vehicle

## Slide 11
Scope and Motivation
Recovery Strategies
Performance Model
Cost Model
Tradeoffs & Comparisons

## Slide 12: Classifying recovery strategies
Choice | Option 1 | Option 2 | Option 3 | Option 4 | Option 5
Portion of booster recovered | Fraction of booster mass recovered: Full: Partial, engines: |  |  |  | 
Recovery location | Launch site | Downrange - ocean | Downrange - ship | Downrange - land | Downrange - mid-air
Recovery propulsion method | Rocket | Air-breathing | None |  | 
Landing method | Propulsive (vertical) | Winged (horizontal) | Parachute |  | 
Choice | Option 1 | Option 2 | Option 3 | Option 4 | Option 5
Portion of booster recovered |  |  |  |  | 
Recovery location | Launch site | Downrange - ocean | Downrange - ship | Downrange - land | Downrange - mid-air
Recovery propulsion method | Rocket | Air-breathing | None |  | 
Landing method | Propulsive (vertical) | Winged (horizontal) | Parachute |  | 
90 possible choice combinations, of which 36 pass “laugh test”
Classification captures all 10 operated or proposed recovery strategies known to the authors

## Slide 13: Identifying recovery strategies
Rocket
Air-breathing
None
Launch site
Propulsive (vertical)
Winged (horizontal)
Insufficient energy for return if staging velocity > ~1 km/s
Parachute
Recovery Propulsion Method
Recovery Location
Landing Method
Downrange - ocean
Downrange - ship
e.g. Falcon 9
e.g. USAF RBS
High landing loads
Propulsive (vertical)
Winged (horizontal)
Parachute
Winged landing preferable
e.g. Baikal, LFBB
High landing loads
Rocket
Air-breathing
None
Propulsion not needed
Propulsive (vertical)
Winged (horizontal)
Parachute
e.g. Shuttle, Ares I
Rocket
Air-breathing
None
Propulsive (vertical)
Winged (horizontal)
Parachute
e.g. Falcon 9
Targeting difficult
Propulsion not needed for winged vehicles
Propulsive (vertical)
Winged (horizontal)
Parachute
e.g. New Glenn
Only small boosters
Full Recovery Partial Recovery
e.g. Adeline
Plausible
Plausible
Plausible
Propul. not needed for winged vehicles
Plausible
Plausible
Plausible
Plausible
Targeting difficult
Only small boosters
Targeting difficult
Plausible
Portion of Booster Recovered
Operated
Plausible
Major challenges
Not desirable
Color code:
e.g. Kistler K-1

## Slide 14: Identifying recovery strategies (2)
Downrange - land
Downrange – mid-air
Rocket
Air-breathing
None
Propulsion not needed
Propulsive (vertical)
Winged (horizontal)
Parachute
Plausible
None
Propulsive (vertical)
Winged (horizontal)
Parachute
e.g. Sippel et al 2017
Plausible
High landing loads
Rocket
Air-breathing
Propulsion not needed
Capture difficult
e.g. ULA SMART
Only small boosters
Recovery Propulsion Method
Recovery Location
Landing Method
Full Recovery Partial Recovery
Portion of Booster Recovered
Plausible
e.g. XS-1 Phantom Express
Operated
Plausible
Major challenges
Not desirable
Color code:

## Slide 15: Identifying recovery strategies (3)
Launch site recovery
Downrange recovery
Falcon 9
USAF RBS
Baikal
Falcon 9
New Glenn
Ares I
XS-1 Phantom Express
Vulcan SMART
Examples:

## Slide 16
Scope and Motivation
Recovery Strategies
Performance Model
Cost Model
Tradeoffs & Comparisons

## Slide 17: Key performance metric is (overall) payload mass fraction
We care about payload mass fraction because:
  It determines how large of a rocket we need to launch a payload to orbit
  Larger rockets are (general) more expensive
Payload,
2nd stage propellant
1st stage propellant
2nd stage inert
1st stage inert
Gross liftoff mass
+
=
Overall payload mass fraction:
Typically, 1% to 6%

## Slide 18: Payload mass fraction depends on:
Mission
  : delta-v required to reach the target orbit (includes grav. & drag losses)
Vehicle design
  : each stage’s (average) specific impulse
  : each stage’s inert mass fraction
  : stage 2 / stage 1 mass ratio

## Slide 19: Tsiolkovsky’s rocket equation relates to mission and vehicle design parameters
delta-v to target orbit
specific impulse
Inert mass fractions
Stage payload mass fractions
Higher
Lower
TODO real numbers
Stage mass ratio
Overall payload mass fraction
Overall payload mass fraction
Delta-v to reach target orbit
LEO
GTO

## Slide 20: “Technology choice” sets and
To maximize payload , we want:
  specific impulse
  inert mass
However, and are constrained by propulsion and structural technology. They depend on:
  Propellants, engine cycle, tank materials & construction, …
We call these factors the “technology choice”
  Always compare reusable & expendable vehicles under the same technology choice assumptions
We’ll examine typical values for
  Kerosene/O2
  H2/O2

## Slide 21: How does reuse change the equation?
Increases 1st stage “inert” mass
  Extra hardware for recovery
  Propellant held in reserve for recovery
Changes to reach target orbit
  Alters gravity and drag losses
  Different ascent profile
  Different vehicle outer mold line
“The impact of the different [reusable launch vehicle] types on the ascent flight profile is found small and, similar to the [expendable launch vehicle] ascent flight performance losses, these are more dependent on the particular configuration […] than on the landing and return modes”
-Sippel, Stapert, Bussler & Dumont, DRL, 2017
Main effect

## Slide 22: Additional mass on a reusable first stage
1st stage propellant
1st stage baseline hardware
Recovery hardware
Recovery propellant

## Slide 23: With recovery, a larger fraction of the 1st stage mass is unavailable for the ascent burn
Launch
Stage separation
Landing
1st stage ascent:
burns
delivers
Recovery:
burns
2nd stage:
delivers

## Slide 24: First stage “unavailable mass” captures performance impacts of recovery
1st stage propellant
1st stage baseline hardware
Recovery hardware
Recovery propellant
of the 1st stage mass is expended during ascent
: recovery adds mass to first stage
Unavailable mass fraction :
Baseline inert mass fraction :
Limited by technology choice
Depends on technology choice
and recovery strategy

## Slide 25: Payload capacity declines as unavailable mass increases

## Slide 26: Unavailable mass depends on:
How much of the first stage we recover:
How much recovery hardware is added:
How much propellant is burned during recovery:
or
=
Rocket propulsion
Air-breathing
propulsion

## Slide 27
Propulsive
Launch site
Winged
Launch site
Winged
Downrange
Parachute
Downrange

## Slide 28: Monte Carlo simulation
Distributions on from recent launch vehicles
Distributions on recovery hardware from detailed design studies and analogies to aircraft
Distributions on recovery propellant from estimates of recovery or recovery cruise range

## Slide 29
TODO shouldn’t extend above max. expendable

## Slide 30
Scope and Motivation
Recovery Strategies
Performance Model
Cost Model
Tradeoffs & Comparisons

## Slide 31: Cost model: Transcost 8.2
Goal: Implement the Transcost 8.2 model to estimate production, development, and operations costs, as well as the total cost-per-flight for various launch vehicles
Validate using operational launch vehicles
Considerations:
  Account for uncertainties in CER coefficients and exponents
  Account for uncertainties in cost factors
  Choose reasonable production numbers (impacts learning effect)

## Slide 32: Production cost estimates for current launch vehicles

## Slide 33: Production cost analysis
Relative cost trends of the vehicles is reasonable (i.e. Falcon 9 costs less than the others)
Production cost estimate values seem to be too high given current listed prices per launch
Possible explanations:
  Launches are underpriced
  Work-Year dollar values are less than industry standard
  Learning factor is better than anticipated
  Scope and profit of subcontractors is less than expected
  Mass of shrouds, fairings, or other components are accounted for improperly

## Slide 34
Scope and Motivation
Recovery Strategies
Performance Model
Cost Model
Tradeoffs & Comparisons

## Slide 35: Performance sensitivity/sweeps
TODO: methane?

## Slide 36: Schedule and launch rate considerations
TODO
Schedule and ops are a key point: reuse may enable higher launch rate with same workforce
Effect of downrange vs. launch site recovery on schedule & fleet size
Effect of partial recovery re-integration on schedule

## Slide 37: Mission/market sensitivities
TODO
Market may soon support high launch rates to LEO due to proposed constellations, eg starlink, oneweb, DARPA blackjack
  Reuse from LEO mission easier than from GTO
  Constellation customers may be more tolerant of launch risk than expensive monolithic satellite customers
Small sat launchers
  Hardware smaller fraction of total cost